## Slide 1: Classical Logic Gates
From Bits to Quantum Leaps Lesson 1

## Slide 2: What are logic gates?
Logic gates are like tiny switches that control the flow of information in computers and other electronic devices.
They are the building blocks of digital circuits, which are the foundation of everything from smartphones to spacecraft.
Imagine a computer as a giant network of these tiny switches, all working together to process information.
These gates work based on a simple idea: they have inputs and outputs, and the output depends on the combination of inputs.
Think of them like a light switch – it can be either on or off, representing a 1 or a 0 in the world of computers. These 1s and 0s are called binary digits, or bits, and they are the language of computers.

## Slide 3: What are logic gates?
There are many different types of logic gates, each with its own unique function.
Some of the most basic ones include the AND gate, the OR gate, and the NOT gate.
    The AND gate only outputs a 1 if all of its inputs are 1.
    The OR gate outputs a 1 if at least one of its inputs is a 1.
    The NOT gate simply inverts its input, meaning if the input is 1, the output is 0, and vice versa.

## Slide 4: Truth Tables
A truth table is a simple way to show how a logic gate works.
Truth tables specify the output (0 or 1) of logic gates, depending on what is applied to its input resp. inputs.
You can think of them as the rules of a game: depending on what the players do (inputs), the result (output) changes!
Usually, the first two columns show the values for two inputs (‘1’ or ‘0’, sometimes ‘true’ or ‘false’ instead) and the third column shows the output value returned by the logic gate.

## Slide 5: Truth Tables
NOT inverts the input.
AND GATE |  | 
INPUT |  | OUTPUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR GATE |  | 
INPUT |  | OUTPUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
NOT Gate | 
INPUT | OUTPUT
1 | 0
0 | 1
OR gives a true output when at least one input is true.
AND gives a true output only when both inputs are true.

## Slide 6: Truth Tables
XOR, which stands for "exclusive OR," is a special type of logic gate. It outputs true (1) only when one of the inputs is true, but not both.
NAND GATE |  | 
INPUT |  | OUTPUT
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR GATE |  | 
INPUT |  | OUTPUT
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR is the inversion
of OR.
NAND is the inversion of AND.
XOR GATE |  | 
INPUT |  | OUTPUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 7: Combination of Gates
These basic gates can be combined in different ways to create more complex functions.
For example, the NAND gate is like an AND gate followed by a NOT gate, and the NOR gate is like an OR gate followed by a NOT gate.
These combinations allow us to build circuits that can perform more complex operations, like adding numbers or comparing values.
Logic gates are essential for the functioning of all digital devices.
By understanding how logic gates work, we can gain a deeper appreciation for the complex world of digital electronics.

## Slide 8: Summary
Logic gates are like tiny switches that control information flow in computers and other devices.
They work with inputs and outputs, using 1s and 0s (binary digits) to represent information.
Different types of logic gates, like AND, OR, and NOT, can be combined to create complex functions and circuits

## Slide 9: Activities
Worksheet Introductory Level
Worksheet Advanced Level
Logic Gate Simulator